## Slide 1: Design Quality Process

## Slide 2: Guiding Standards
ISO 13485 - Medical devices -- Quality management systems
  Standards that guides the development of medical devices
  Voluntary Standard
  Covers Organization, Human resources, Quality documentation system, design/development, manufacturing, parts sourcing…
We are focusing on complying with design and development so that the design is well documented.
This will allow us to quickly transition the design to a manufacturing partner and adhere to regulatory standards.
The manufacturing partner or marketing partner is ultimately responsible for quality

## Slide 3: Project Phases
Planning
  Design Development/Quality Plan – defines how the project will be performed and what deliverables there will be in each phase
  User Needs / Design Inputs – What do we want the product to do
  Preliminary Risk Analysis
Design Development
  Where the design takes place
  Deliverables are subsystem requirements (software, electrical)
  Design Risk Analysis (DFMEA)
  Design Outputs – Specifications (CAD, schematic, source code and design reviews)
Verification
  Activities showing that requirements were met and works as intended. Includes protocols with established criterion
Validation
  Activities which show that user needs were met. Addresses clinical use.
Design Transfer – The transfer to manufacturing (will be handled later)

## Slide 4: Documentation
The records of the design go into a Design History File (DHF)
These documents will be kept in a separate location from the general development files
  Approved Requirements
  Risk Analysis
  Final Design Outputs
  Verification Protocols and Reports
Phase Reviews
  At the end of each phase there will be a phase review which shows that all deliverables were met.

## Slide 5: Software Quality
IEC 62304 Provides a guideline on the software development lifecycle
Requires Established Lifecycle Plan with the following
  Software Architecture – High level description
  Software Detailed Design – Unit/Module level documentation
  Software Development Environment definition – IDE/compiler etc..
  Software Risk Analysis
  Software Requirements
  Software Unit Testing
  Software Integration Testing
  Software Validation

## Slide 6: Our Approach
Initial prototype development can continue without all processes in place.
We should do enough to ensure that the design is safe and controlled
  Risk Analysis should be complete and design outputs should be frozen
  Verification should be done to ensure that there are no issues.
As we near the need for the next phase we can evaluate and determine what documentation we need to close out the current phase. Quality people will make sure that documentation is transferred to a controlled location and labelled.
The compliance is ultimately up to the company marketing the product.
Regulatory requirements vary country to country and are also relaxed in time of emergency.